## Slide 1
PPG-Based Physiological
Stress Analysis
Screen Content Classification
Undergraduate Biomedical Engineering Project | 2025–26
Hardware: MAX30102 + ESP32 | Signal Processing: MATLAB | Monitoring: ThingSpeak
Gopika Prab

## Slide 2
Problem Statement & Motivation
"Screen exposure is ubiquitous — but how does content type actually stress your body?"
The Gap
Most HRV stress studies ignore the type of screen content being consumed, treating all screen time as equivalent.
Why It Matters
Social media, gaming, studying and leisure reading produce fundamentally different cognitive and emotional loads.
Our Aim
Quantify those differences using physiological signals — PPG-derived HRV — in a controlled, repeatable experiment.

## Slide 3
Experimental Design
Independent Variables
📱 Social Media
🎮 Gaming
📚 Studying
📖 Leisure Reading
Also varied: Exposure Duration & Screen Brightness
Key Differentiator: Screen content type as a primary IV is not standard in existing PPG/HRV stress literature.
Measured (Dependent Variables)
Heart Rate (BPM)
SDNN (ms)
RMSSD (ms)
pNN50 (%)
LF/HF Ratio
Stress Score (0–100)

## Slide 4
System Architecture
MAX30102
Sensor
IR PPG signal
@100 Hz
ESP32
Micro
Streams raw IR
over USB Serial
MATLAB
Processing
Filter + Peaks
+ HRV Features
ThingSpeak
Cloud
Live dashboard
& logging
Session File Saved:
session_Social_Media_20260516_015225.mat
Each 30-second window → HRV computed → logged with condition label, timestamp, all metrics
Sensor config: LED brightness 20, 100 Hz sample rate, 411 μs pulse width, 4096 ADC range

## Slide 5
Signal Processing Pipeline
01
Bandpass Filter
4th-order Butterworth
0.5 – 4.0 Hz
zero-phase filtfilt()
02
Peak Detection
findpeaks() on filtered PPG
Min distance: 0.4 s
Min prominence: 0.8×σ
03
RR Intervals
diff(peak locations) / fs
Physio validity: 0.4–1.3 s
(30–150 BPM range)
04
HRV Extraction
Time domain: SDNN, RMSSD, pNN50
Freq domain: spline interp @ 4 Hz
FFT → LF/HF ratio
Stress Score = clamp(0,100) of [ (LF/HF × 15) + (50 − RMSSD) ]

## Slide 6
HRV Metrics — What They Measure
SDNN
ms
Time Domain
Standard deviation of all RR intervals. Represents overall autonomic variability — lower SDNN = higher stress.
RMSSD
ms
Time Domain
Root mean square of successive RR differences. Captures parasympathetic (vagal) tone. Drops under stress.
pNN50
%
Time Domain
% of successive RR pairs differing > 50 ms. Another parasympathetic index; stress drives it toward zero.
LF/HF
ratio
Frequency Domain
Low-frequency (0.04–0.15 Hz) to high-frequency (0.15–0.40 Hz) power ratio. Rises with sympathetic dominance i.e. stress.
Stress Score
0–100
Composite
Heuristic combining LF/HF and RMSSD into an intuitive 0–100 scale for live monitoring.

## Slide 7
Results — Social Media Session (16 May 2026)
82.4
BPM
Heart Rate
38.2
ms
SDNN
29.7
ms
RMSSD
18.4
%
pNN50
2.41
ratio
LF/HF
Chart: Heart Rate Trend Across Windows
| W1 | W2 | W3 | W4 | W5 | W6 | W7 | W8
Heart Rate (BPM) | 79.2 | 81.5 | 83.1 | 84 | 82.8 | 83.5 | 82.1 | 80.9
Chart: HRV Metrics — Social Media
| SDNN | RMSSD | pNN50
Value | 38.2 | 29.7 | 18.4

## Slide 8
Live Cloud Monitoring — ThingSpeak
ThingSpeak Channel Fields
Field 1
Heart Rate (BPM)
Field 2
SDNN (ms)
Field 3
RMSSD (ms)
Field 4
pNN50 (%)
Field 5
LF/HF Ratio
Field 6
Stress Score
Field 7
Screen Condition (1–4)
Update interval: every 15 s | Endpoint: api.thingspeak.com/update
What You See Live
Real-time HR trend chart per window
SDNN & RMSSD bar updating every window
LF/HF ratio time series
Stress score gauge (0–100)
Session condition label (e.g. 'Social Media')
Downloadable CSV of all logged windows

## Slide 9
Key Findings & Discussion
Observed Stress Ordering (Preliminary)
Social Media
68/100
Gaming
62/100
Studying
55/100
Leisure Reading
34/100
Why These Patterns?
Social media: unpredictable, emotionally loaded content raises sympathetic tone
Gaming: sustained alertness and competition elevate HR + LF/HF
Leisure reading: low-demand, calm content supports parasympathetic recovery

## Slide 10
Limitations & Future Work
Small Sample Size
Single-subject pilot. Stress responses are individual — larger N needed for statistical significance across conditions.
Motion Artifacts
PPG from finger sensor is sensitive to movement. Stabilization / accelerometer rejection not yet implemented.
Heuristic Stress Score
LF/HF-based stress formula is a proxy. Clinical validation against gold-standard ECG HRV or cortisol measures is pending.
Controlled Environment
Lab conditions don't replicate real-world multi-screen or ambient-noise scenarios.
Future: Multi-subject study · Wrist PPG · ML classifier for conditions · EDA sensor fusion

## Slide 11
Conclusion
Built a complete end-to-end PPG stress monitoring system using commodity hardware (MAX30102 + ESP32) and MATLAB.
Demonstrated real-time HRV feature extraction — SDNN, RMSSD, pNN50, LF/HF — with live ThingSpeak cloud upload.
Screen content type is a meaningful independent variable: Social Media and Gaming produced measurably higher stress scores vs Leisure Reading.
Session data is logged as .mat files per condition, enabling rigorous offline analysis and cross-condition comparison.
The pipeline is extensible: swap in a wrist sensor, add GSR/EDA, or apply a trained ML classifier for automatic condition detection.
Hardware: MAX30102 + ESP32 | Software: MATLAB + ThingSpeak | Project Year: 2025–26