## Slide 1
BIOMEDICAL SIGNAL PROCESSING
Physiological Stress Analysis
Using PPG Signals During Screen Interaction
Measuring cardiovascular stress indicators through HRV analysis
during prolonged digital device exposure
Department of Biomedical Engineering | Undergraduate Project | 2025-26

## Slide 2
Introduction
The Problem
Screen time has increased dramatically worldwide.
Prolonged digital device usage may cause:
Elevated stress levels
Mental fatigue
Autonomic nervous system imbalance
Current methods rely on self-reports which are subjective. Physiological signals provide objective measurement.
Our Approach
We use PPG signals to objectively measure stress.
Two signal types combined:
Medical: PPG (Photoplethysmography)
Behavioral: Screen interaction data
Key metric extracted: Heart Rate Variability (HRV)
Goal: Determine if screen exposure changes cardiovascular stress indicators.
Physiological Stress Analysis Using PPG Signals

## Slide 3
Core Signals Used
Medical Signal: PPG
Photoplethysmography (PPG)
Measures blood volume changes using light reflection from skin.
Sensors:
MAX30102 (recommended)
Pulse Sensor (simpler option)
Provides:
Heart rate
Pulse waveform
Beat intervals (for HRV)
Behavioral Signal: Screen
Screen Interaction Metrics
Acts as the external stimulus/condition applied during experiments.
Possible Metrics:
Total screen usage duration
Screen brightness level
Continuous interaction period
Research Questions:
Does screen time change heart rate?
Does HRV decrease with longer usage?
Does brightness influence stress?
Physiological Stress Analysis Using PPG Signals

## Slide 4
System Architecture & Block Diagram
Screen
Interaction
(Stimulus)
PPG Sensor
(MAX30102)
Microcontroller
(ESP32/
Arduino)
Data
Acquisition
Signal
Processing
& Filtering
HRV Feature
Extraction
Analysis &
Comparison
External Condition
Hardware Layer
Software Processing Layer
Hardware Components
Sensor: MAX30102 or Pulse Sensor
Microcontroller: ESP32 (recommended) or Arduino UNO
Computer for signal processing & visualization
Software Tools
MATLAB — excellent for signal processing & plotting
Python — NumPy, SciPy, Matplotlib libraries
Both tools are equally suitable for this project
Physiological Stress Analysis Using PPG Signals

## Slide 5
Signal Processing Methodology
01
Data
Acquisition
Raw PPG signal at 50-100 Hz sampling rate via ESP32/Arduino
->
02
Filtering
Butterworth low-pass filter removes motion artifacts, noise, baseline drift
->
03
Peak
Detection
Identify heartbeat peaks using findpeaks (MATLAB) or scipy.find_peaks (Python)
->
04
RR Interval
Calc.
Calculate time difference between consecutive detected heartbeat peaks
->
05
HRV
Extraction
Compute: Mean RR, SDNN (overall variability), RMSSD (stress metric)
Key Insight: Higher HRV = Relaxed State | Lower HRV = Stress or Fatigue
Physiological Stress Analysis Using PPG Signals

## Slide 6
Experimental Design
Baseline
Duration:
~5 min rest
Subject is relaxed with no screen interaction. PPG recorded to establish baseline HRV values.
Short Exposure
Duration:
~5 minutes
Subject interacts with a screen for 5 minutes. PPG recorded during interaction period.
Prolonged Exposure
Duration:
20-30 minutes
Continuous screen interaction for 20-30 minutes. PPG recorded throughout entire session.
Optional: Brightness
Duration:
Varies
Compare low vs high screen brightness effect on HRV and physiological stress response.
Physiological Stress Analysis Using PPG Signals

## Slide 7
Expected Results & Data Analysis
Condition | HRV Level | Heart Rate | Stress Estimate
Baseline (No screen) | HIGH | Normal | Low
Short Exposure (~5 min) | MODERATE | Slightly elevated | Moderate
Long Exposure (20-30 min) | LOW | Elevated | Higher
Key Expected Observations
1
Prolonged screen interaction reduces HRV — indicating higher physiological stress
2
Increased heart rate observed after extended screen use
3
Reduced variability in heartbeat intervals with longer exposure
Physiological Stress Analysis Using PPG Signals

## Slide 8
Our Project Plan
Signal / Data Source
PPG sensor (MAX30102) connected to ESP32
Real-time data streamed to computer
Sampling rate: 50-100 Hz
Analysis Approach
Time-domain HRV: Mean RR, SDNN, RMSSD
Compare baseline vs screen exposure conditions
Butterworth filter for noise removal
Additional Work
Brightness variation experiment (low vs high)
Live real-time PPG visualization demo
Comparative plots across all conditions
Final Deliverables:
Hardware setup & signal acquisition system
Signal processing code (MATLAB or Python)
Experimental data, analysis results & live demonstration
Physiological Stress Analysis Using PPG Signals

## Slide 9
References
1
IEEE Xplore (6908199) — PPG-based heart rate monitoring
2
IEEE Xplore (10605974) — HRV analysis in stress detection
3
IEEE Xplore (4353036) — Digital filtering of biomedical signals
4
IEEE Xplore (7032208) — Wearable sensors for physiological monitoring
5
IEEE Xplore (9844174) — Screen exposure and autonomic response
6
IEEE Xplore (4671121) — Photoplethysmography signal processing
Thank You